## Slide 1: COE211: Digital Logic Design
Introduction

## Slide 2: * Introduction to Digital Logic Design
One of the characteristics that separates an engineer or computer scientist from a layperson (not professional) is a systematic approach to managing complexity.
Modern digital systems are built from millions or billions of transistors.
No human being could understand these systems by writing equations describing the movement of electrons in each transistor and solving all of the equations simultaneously.
You will need to learn to manage complexity to understand how to build a microprocessor by easily manner.

## Slide 3: * Levels of abstraction for electronic computing system

## Slide 4: * Digital and Analog Quantities
An analog quantity is one having continuous values
A digital quantity is one having a discrete set of values

## Slide 5: * An Analog Electronic System

## Slide 6: * A System Using Digital and Analog Methods

## Slide 7: * Basic Logic States

## Slide 8: * Basic Logic Operations

## Slide 9: * Basic Logic Operations

## Slide 10: Digital Computer Systems
Digital systems consider discrete amounts of data
Examples
  26 letters in the alphabet
  10 decimal digits
Larger quantities can be built from discrete values:
  Words made of letters
  Numbers made of decimal digits (e.g. 239875.32)
Computers operate on binary values (0 and 1)
Easy to represent binary values electrically
  Voltages and currents
  Can be implemented using circuits
  Create the building blocks of modern computers

## Slide 11: Number Systems
Decimal Numbers
Binary Numbers
Octal Numbers
Hexadecimal Numbers
Number System Conversion
Signed Number Representation

## Slide 12: Understanding Decimal Numbers
Decimal numbers are made of decimal digits: (0,1,2,3,4,5,6,7,8,9)  Base = 10
But how many items does a decimal number represent?
  8653 = 8 x103 + 6 x102 + 5 x101 + 3 x100
  Number = d3 x B3 + d2 x B2 + d1 x B1 + d0 x B0 = Value
What about fractions?
  97654.35 = 9x104 + 7x103 + 6x102 + 5x101 + 4x100 + 3x10-1 + 5x10-2
  In formal notation → (97654.35)10

## Slide 13: * Understanding Decimal Numbers
Example

## Slide 14: Understanding Binary Numbers
Binary numbers are made of binary digits (bits):
  0 and 1
How many items does a binary number represent?
  8 4 2 1 = Weights
  (1011)2 = 1x23 + 0x22 + 1x21 + 1x20 = (11)10
What about fractions?
  (110.10)2 = 1x22 + 1x21 + 0x20 + 1x2-1 + 0x2-2
Groups of eight bits are called a byte
  (11001001)2
Groups of four bits are called a nibble
  (1101)2

## Slide 15: * Understanding Binary Numbers
POSITIVE POWERS OF TWO (WHOLE NUMBERS) |  |  |  |  |  |  |  |  | NEGATIVE POWERS OF TWO (FRACTIONAL NUMBER) |  |  |  |  | 
28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 2-1 | 2-2 | 2-3 | 2-4 | 2-5 | 2-6
256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 1/2 | 1/4 | 1/8 | 1/16 | 1/32 | 1/64
 |  |  |  |  |  |  |  |  | 0.5 | 0.25 | 0.125 | 0.0625 | 0.03125 | 0.015625

## Slide 16: Understanding Octal Numbers
Octal numbers are made of octal digits: (0,1,2,3,4,5,6,7)
How many items does an octal number represent?
  512 64 8 1 = Weights
  (4536)8 = 4x83 + 5x82 + 3x81 + 6x80 = (2398)10
What about fractions?
  (465.27)8 = 4x82 + 6x81 + 5x80 + 2x8-1 + 7x8-2
Octal numbers don’t use digits 8 or 9

## Slide 17: Understanding Hexadecimal Numbers
Hexadecimal numbers are made of 16 digits:
  (0,1,2,3,4,5,6,7,8,9,A, B, C, D, E, F)
How many items does a hex number represent?
4096 256 16 1 = Weights
  (3A9F)16 = 3x163 + 10x162 + 9x161 + 15x160 = 1500710
What about fractions?
  (2D3.5)16 = 2x162 + 13x161 + 3x160 + 5x16-1 = 723.312510
Note that each hexadecimal digit can be represented with four bits
  (1110)2 = (E)16

## Slide 18: Why Use Binary Numbers?
Easy to represent 0 and 1 using electrical values
Possible to tolerate noise
Easy to transmit data
Easy to build binary circuits
AND Gate
1
0
0

## Slide 19: Convert an Integer from Decimal to Another Base
Divide decimal number by the base (e.g. 2)
The remainder is the lowest-order digit
Repeat first two steps until no divisor remains
For each digit position:
Example for (13)10:
Quotient
13/2 = 6 , 1 a0 = 1
6/2 = 3 , 0 a1 = 0
3/2 = 1 , 1 a2 = 1
1/2 = 0 , 1 a3 = 1
Remainder
Coefficient
Answer (13)10 = (a3 a2 a1 a0)2 = (1101)2
MSB LSB

## Slide 20: * Convert an Integer from Decimal to Binary
MSB
LSB
MSB
LSB
95
47
23
11
5
2
1
0
1
1
1
1
1
0
1
2
2
2
2
2
2
2
= 1 0 1 1 1 1 1
÷
64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
64 | 0 | 16 | 8 | 4 | 2 | 1
* Convert from Binary to Decimal

= 95

## Slide 21: Convert a Fraction from Decimal to Another Base
Multiply decimal number by the base (e.g. 2)
The integer is the highest-order digit
Repeat first two steps until fraction becomes zero
For each digit position:
Example for (0.625)10:
Integer
0.625 x 2 = 1 + 0.250 a-1 = 1
0.250 x 2 = 0 + 0.500 a-2 = 0
0.500 x 2 = 1 + 0 a-3 = 1
Fraction
Coefficient
Answer (0.625)10 = (0.a-1 a-2 a-3 )2 = (0.101)2
MSB LSB

## Slide 22: * Convert an Integer from Decimal to Binary
MSB
LSB
MSB
LSB
0.33203125.
0.6640625
0.328125
0.65625
0.3125
0.625
0.25
0.5
0
0
1
0
1
0
1
0
1
2
2
2
2
2
2
2
2
= 0.01010101

0.5 | 0.25 | 0.125 | 0.0625 | 0.03125 | 0.015625 | 0.0078125
0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 0.25 | 0 | 0.0626 | 0 | 0.015625 | 0
* Convert from Binary to Decimal

= 0.3320303125
0.00390625
1
0.00390625

## Slide 23: * Conversion Between Base 16 and Base 2
Decimal Number | Binary Number |  |  | 
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0
7 | 0 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1
Hexadecimal Number
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F

## Slide 24: Conversion Between Base 16 and Base 2
Conversion is easy!
  Determine the 4-bit value for each hex digit
Note that there are 16 different values of four bits
Easier to read and write in hexadecimal
Representations are equivalent!
3A9F16 = 0011 1010 1001 11112
3
A
9
F

## Slide 25: * Example
Convert the following binary numbers to hexadecimal:
(a) 1100101001010111
(b) 111111000101101001
Solution.
1100 _ 1010 _ 0101 _ 0111 = CA57)16
0011 _ 1111 _ 0001 _ 0110 _ 1001 = 3F169)16

## Slide 26: The Growth of Binary Numbers

## Slide 27: * Hexadecimal-to-Decimal Conversion
163 162 161 160
4096 256 16 1
Convert the following hexadecimal numbers to decimal:
(a) E5)16 (b) B2F8)16
Solution.
(a) E5)16 = (E16) + (51) = (1416) + (51) = 224 + 5 = 229)10
(b) B2F8)16 = (B4096) + (2256) + (F16) + (81) = (114096) + (2256) + (1516) + (81) = 45,056 + 512 + 240 + 8 = 45,81610

## Slide 28: * Decimal-to-Hexadecimal Conversion
Convert the decimal number 650 to hexadecimal by repeated division by 16.
Solution.

## Slide 29: * Octal Numbers
Decimal | Binary |  |  | Octal
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
2 | 0 | 1 | 0 | 2
3 | 0 | 1 | 1 | 3
4 | 1 | 0 | 0 | 4
5 | 1 | 0 | 1 | 5
6 | 1 | 1 | 0 | 6
7 | 1 | 1 | 1 | 7

## Slide 30: * Octal-to-Decimal Conversion
Convert 2374)8 to Decimal
Weight: 83 82 81 80
Octal number: 2 3 7 4
2374)8 = (2  83) + (3  82 ) + (7  81 ) + (4  80)
= (2512) + (3  64) + (7  8) + (4  1)
= 1024 + 192 + 56 + 4 =1276)10

## Slide 31: * Decimal-to-Octal Conversion
Convert 359)10 to Octal

## Slide 32: * Octal-to-Binary Conversion
Convert each of the following octal numbers to binary: (a) 13)8 (b) 25)8 (c) 140)8 (d) 7526)8
Solution.
13 = 001 _ 011 = 1011
25 = 010 _ 101 = 10101
140 = 001_100_000 = 1100000
7526 =111_101_010_110 = 111101010110

## Slide 33: * Hexadecimal-to-Octal Conversion
Convert each of the following numbers:
(a) 7526)8 to Hexadecimal (b) 5AC2)16 to Octal
Solution.
7526)8 =111_101_010_110 = 111101010110
1111_0101_0110 = F56)16
5AC2)16 =0101_1010_1100_0010 = 101101011000010
101_101_011_000_010 = 55302)8

## Slide 34: Understanding Binary Coded Decimal
Binary Coded Decimal (BCD) represents each decimal digit with four bits
  Ex. 0011 0010 1001
This is NOT the same as 0011001010012 = 80910
Digit | BCD Code
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
3
2
9
= 329BCD

## Slide 35: Putting It All Together
Decimal | Binary | Octal | Hexadecimal | BCD
0 | 0000 | 0 | 0 | 000
1 | 0001 | 1 | 1 | 0001
2 | 0010 | 2 | 2 | 0010
3 | 0011 | 3 | 3 | 0011
4 | 0100 | 4 | 4 | 0100
5 | 0101 | 5 | 5 | 0101
6 | 0110 | 6 | 6 | 0110
7 | 0111 | 7 | 7 | 0111
8 | 1000 | 10 | 8 | 1000
9 | 1001 | 11 | 9 | 1001
10 | 1010 | 12 | A | 0001 0000
11 | 1011 | 13 | B | 0001 0001
12 | 1100 | 14 | C | 0001 0010
13 | 1101 | 15 | D | 0001 0011
14 | 1110 | 16 | E | 0001 0100
15 | 1111 | 17 | F | 0001 0101

## Slide 36: * Binary Addition
Carry-in | A | B | Sum | Carry-out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 37: * Binary Addition
1111111
00111011 1+2+8+16+32 = 59
01010111+ 1+2+4+16+64 = 87
------------ = 146
10010010 2+16+128 = 146

## Slide 38: * Binary Subtraction
0 - 0 = 0
1 - 1 = 0
1 - 0 = 1
10 - 1 = 1
0 - 1 with a borrow of (1)

## Slide 39: * 1's and 2's Complements of Binary Numbers
Finding the 1's Complement
Finding the 2's Complement
2's complement = (l's complement) + 1

## Slide 40: * Subtracting two unsigned numbers
1's Complement
 | 01010111 | 
 | 00111011 | -
 | 01010111 | 
 | 11000100 | +
1 | 00011011 | 
 | 1 | 
 | 11100 | 

## Slide 41: * Subtracting two unsigned numbers
2's Complement
 | 01010111 | 
 | 00111011 | -
 | 01010111 | 
 | 11000101 | +
1 | 00011100 | 

## Slide 42: How To Represent Signed Numbers
Plus and minus signs are used for decimal numbers:
  25 (or +25), −16, etc
In computers, everything is represented as bits
Three types of signed binary number representations:
  signed magnitude
  1’s complement
  2’s complement
In each case: left-most bit indicates the sign: ‘0’ for positive and ‘1’ for negative

## Slide 43: Signed Magnitude Representation
000011002 = 1210
Sign bit
Magnitude
100011002 = −1210
Sign bit
Magnitude
The left most bit is designated as the sign bit while the remaining bits form the magnitude

## Slide 44: One’s Complement Representation
The one’s complement of a binary number is done by complementing (i.e. inverting) all bits
  1’s comp of 00110011 is 11001100
  1’s comp of 10101010 is 01010101
For a n-bit number N the 1’s complement is (2n − 1) − N
Called “diminished radix complement” by Mano
To find the negative of a 1’s complement number take its 1’s complement
000011002 = 1210
Sign bit
Magnitude
111100112 = −1210
Sign bit
Code

## Slide 45: One’s Complement Representation
1000
− 7
0000
0
0111
7
.
.
.
.
0110
6
0001
1
1111
− 0
1110
− 1
.
.
.
.
1001
− 6
4 bits
 16 combinations

## Slide 46: Two’s Complement Representation
The two’s complement of a binary number is done by complementing (inverting) all bits then adding 1
  2’s comp of 00110011 is 11001101
  2’s comp of 10101010 is 01010110
For an n-bit number N the 2’s complement is (2n−1) − N + 1
Called “radix complement” by Mano
To find the negative of a 2’s complement number take its 2’s complement
000011002 = 1210
Sign bit
Magnitude
111101002 = −1210
Sign bit
Code

## Slide 47: Two’s Complement Shortcuts
Algorithm 1: Complement each bit then add 1 to the result
  N = 01100101
  10011010
  + 1
    10011011
Algorithm 2: Starting with the least significant bit, copy all of the bits up to and including the first ‘1’ bit, then complement the remaining bits
  N = 0 1 1 0 0 1 1 0
[N] = 1 0 0 1 1 0 1 0
[N] = 10011011
01100100
+ 1
01100101

## Slide 48: Two’s Complement Representation
1000
− 8
0000
0
0111
7
0010
2
.
.
0110
6
0001
1
1111
− 1
1110
− 2
.
.
.
.
1001
− 7
4 bits
 16 combinations

## Slide 49: Putting All Together

## Slide 50: Finite-Precision Number Representation
Machines that use 2’s complement arithmetic can represent integers in the range
− 2n-1 ≤ N ≤ 2n-1 − 1
n is the number of bits used for representing N
Note that 2n-1 − 1 = (011..11)2 and − 2n-1 = (100..00)2
2’s complement code has more negative numbers than positive
1’s complement code has 2 representations for zero
For an n-bit number in base (i.e. radix) z there are zn different unsigned values (combinations)
(0, 1, …zn-1)

## Slide 51: 2’s Complement Addition
Using 2’s complement representation, adding numbers is easy
  Step 1: Add binary numbers
  Step 2: Ignore the resulting carry bit
For example: (12)10 + (1)10
  (12)10 = +(1100)2
  = 011002 in 2’s comp.
  (1)10 = +(0001)2
  = 000012 in 2’s comp.
0 1 1 0 0
+ 0 0 0 0 1
--------------
0 0 1 1 0 1
Final
Result
Add
Ignore

## Slide 52: 2’s Complement Subtraction
Using 2’s complement representation, subtracting numbers is also easy
  Step 1: Take 2’s complement of 2nd operand
  Step 2: Add binary numbers
  Step 3: Ignore the resulting carry bit
For example: (12)10 − (1)10
  (12)10 = +(1100)2
  = 011002 in 2’s comp.
  (−1)10 = −(0001)2
  = 111112 in 2’s comp.
0 1 1 0 0
- 0 0 0 0 1
0 1 1 0 0
+ 1 1 1 1 1
--------------
1 0 1 0 1 1
Final
Result
2’s comp
Add
Ignore
Carry

## Slide 53: 2’s Complement Subtraction (Cont’d)
Example 2: (13)10 − (5)10
  (13)10 = +(1101)2 = (01101)2
  (−5)10 = −(0101)2 = (11011)2
Adding these two 5-bit codes:
    0 1 1 0 1
    + 1 1 0 1 1
    1 0 1 0 0 0
Discarding the carry bit, the sign bit is seen to be zero, indicating a positive result
Indeed: (01000)2 = +(8)10
Carry

## Slide 54: 2’s Complement Subtraction (Cont’d)
Example 3: (5)10 − (12)10
  (5)10 = +(0101)2 = (00101)2
  (−12)10 = −(1100)2 = (10100)2
Adding these two 5-bit codes:
    0 0 1 0 1
    + 1 0 1 0 0
    0 1 1 0 0 1
Here, there is no carry bit and the sign bit is 1. This indicates a negative result, which is what we expect: (11001)2 = – (7)10
Carry

## Slide 55: * Example 1
Add the signed numbers: 01000100, 00011011, 00001110, and 000 10010.
68 01000100
+ 27 + 00011011 ­Add 1st two numbers
------ -------------
95 01011111 1st sum
+ 14 + 00001110 Add 3rd number
----- -------------
109 01101101 2nd sum
+ 18 + 00010010 Add 4th number
----- -------------
127 01111111 Final sum

## Slide 56: * Example 2
Perform each of the following subtractions of the signed numbers:
(a) 00001000 - 00000011 (c) 11100111 - 00010011
(b) 00001100 - 11110111 (d) 10001000 - 11100010
(a) In this case, 8 - 3 = 8 + (-3) = 5.
00001000 Minuend (+ 8)
+ 11111101 2's comp. of subtrahend (- 3)
--------------
Discard carry 1 00000101 Difference ( + 5)

## Slide 57: * Example 2 (Cont’d)
(b) In this case, 12 - (-9) = 12 + 9 = 21.
00001100 Minuend (+ 12)
+ 00001001 2's comp. of subtrahend (+9)
--------------
00010101 Difference ( + 21)
(c) In this case, -25 - (+ 19) = -25 + (-19) = -44.
11100111 Minuend (-25)
+ 11101101 2's comp. of subtrahend (-19)
--------------
Discard carry 1 11010100 Difference ( -44)

## Slide 58: * Example 2 (Cont’d)
(d) In this case, -120 - (-30) = -120 + 30 = -90.
10001000 Minuend (-120)
+ 00011110 2's comp. of subtrahend (+30)
--------------
10100110 Difference (-90)

## Slide 59: Gray Code
Gray code is not a number system
  It is an alternate way to represent four bit data
Only one bit changes from one decimal digit to the next
Useful for reducing errors in communication
Can be scaled to larger numbers
Digit | Binary | Gray Code
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0011
3 | 0011 | 0010
4 | 0100 | 0110
5 | 0101 | 0111
6 | 0110 | 0101
7 | 0111 | 0100
8 | 1000 | 1100
9 | 1001 | 1101
10 | 1010 | 1111
11 | 1011 | 1110
12 | 1100 | 1010
13 | 1101 | 1011
14 | 1110 | 1001
15 | 1111 | 1000

## Slide 60: Text: ASCII Characters
ASCII: Maps 128 characters to 7-bit code.
  both printable and non-printable (ESC, DEL, …) characters http://www.asciitable.com/
00 | nul | 10 | dle | 20 | sp | 30 | 0 | 40 | @ | 50 | P | 60 | ` | 70 | p
01 | soh | 11 | dc1 | 21 | ! | 31 | 1 | 41 | A | 51 | Q | 61 | a | 71 | q
02 | stx | 12 | dc2 | 22 | " | 32 | 2 | 42 | B | 52 | R | 62 | b | 72 | r
03 | etx | 13 | dc3 | 23 | # | 33 | 3 | 43 | C | 53 | S | 63 | c | 73 | s
04 | eot | 14 | dc4 | 24 | $ | 34 | 4 | 44 | D | 54 | T | 64 | d | 74 | t
05 | enq | 15 | nak | 25 | % | 35 | 5 | 45 | E | 55 | U | 65 | e | 75 | u
06 | ack | 16 | syn | 26 | & | 36 | 6 | 46 | F | 56 | V | 66 | f | 76 | v
07 | bel | 17 | etb | 27 | ' | 37 | 7 | 47 | G | 57 | W | 67 | g | 77 | w
08 | bs | 18 | can | 28 | ( | 38 | 8 | 48 | H | 58 | X | 68 | h | 78 | x
09 | ht | 19 | em | 29 | ) | 39 | 9 | 49 | I | 59 | Y | 69 | i | 79 | y
0a | nl | 1a | sub | 2a | * | 3a | : | 4a | J | 5a | Z | 6a | j | 7a | z
0b | vt | 1b | esc | 2b | + | 3b | ; | 4b | K | 5b | [ | 6b | k | 7b | {
0c | np | 1c | fs | 2c | , | 3c | < | 4c | L | 5c | \ | 6c | l | 7c | ¦
0d | cr | 1d | gs | 2d | - | 3d | = | 4d | M | 5d | ] | 6d | m | 7d | }
0e | so | 1e | rs | 2e | . | 3e | > | 4e | N | 5e | ^ | 6e | n | 7e | ~
0f | si | 1f | us | 2f | / | 3f | ? | 4f | O | 5f | _ | 6f | o | 7f | del