## Slide 1: COE211: Digital Logic Design
Synchronous Sequential Logic
Part 2:
Sequential Circuits Analysis and Design

## Slide 2: Analysis of Sequential Circuits
Behavior of clocked sequential circuit determined by
  Inputs
  Outputs
  State of flip-flops
Analysis process
  Consider all combinations of
    Inputs
    Flip-flop states
  Determine next state and output of circuit
Concept of a Finite State Machine (FSM)
Methods
  State equations
  State table
  State diagram

## Slide 3: Example Circuit
Sequential circuit
  Input: x
  Output: y
  Flip-flops:
    2 D-type FFs
    A and B
When is y=1?
  Very difficult to answer
  Systematic analysis
  necessary

## Slide 4: State and Output Equations
Circuit view FSM view

## Slide 5: State and Output Equations
State equation specifies next state
  Function of current state and inputs
State equation for flip-flops:
  A(t+1) = A(t) x(t) + B(t) x(t)
  B(t+1) = A’(t) x(t)
Output expression:
  y(t) = (A(t) + B(t)) x’(t)
Simplified notation:
  A(t+1) = A x + B x
  B(t+1) = A’ x
  y = (A+B) x’
How to derive these Eqs?

## Slide 6: Flip-flop Input Equations
Similar to state equations
  Specifies type of flip-flop used
  In case of D-FFs
  they are the
  same as state equations.
This circuit:
  DA = A x + B x
  DB = A’ x
  y = (A + B) x’

## Slide 7: State Table
What needs to be considered in table?
  Inputs
  State of flip-flops
  Next state of flip-flops
  Outputs
How many entries in state table?
  n inputs
  m number of flip-flops
  Total of 2m+n entries
For every entry
  Determine flip-flop change by input and current state
    State equation
  Determine the output (Output equation)

## Slide 8: State Table
  A(t+1) = A x + B x
  B(t+1) = A’ x
  y = (A+B) x’

## Slide 9: State Table

## Slide 10: State Diagram
State transitions represented as graph
  Vertices indicate states
  Edges represent transitions
    Edge annotation: “x/y” meaning input is x and output is y

## Slide 11: Analysis Example 2
  Equation:
  (state equation)
  (flip-flop equation)
State table:
State diagram:
  Note: no outputs

## Slide 12: Analysis with JK FF
Flip-flop Input Equations

## Slide 13: Analysis with JK FF
State Equations

## Slide 14: Analysis with JK FF
State Equations
State table:
State Diagram:

## Slide 15: Finite State Machines
State diagrams are representations of Finite State Machines (FSM)
Two flavors of FSMs:
  Mealy FSM
  Moore FSM
Difference:
  How output is determined
Mealy FSM
  Output depends on input and state
  Output is not synchronized with clock
  can have temporarily unstable output
Moore FSM
  Output depends only on state

## Slide 16: Mealy vs Moore Machine
Mealy Machine
  Output is a function of
  current state and present input
Moore Machine
  Output is a function of
  current state only

## Slide 17
Design of Sequential Circuits

## Slide 18: Design of Sequential Circuits
Derive state diagram from description
  Reduce number of states if necessary (will NOT be covered)
Assign binary values to states
Obtain binary coded state table (transition table)
Choose type of flip-flops
Derive flip-flop input equations and output equations
Draw logic diagram

## Slide 19: Example 1: Sequence Detector
Circuit specification:
  Design a circuit that outputs a 1 when three consecutive 1s have been applied to input, and 0 otherwise.”
Step 1: derive state diagram
  What should a state represent?
    E.g., “number of 1’s seen so far”
  Moore or Mealy FSM?
    Both possible
    Chose Moore to simplify diagram
  State diagram:
    State S0: zero 1s detected
    State S1: one 1 detected
    State S2: two 1s detected
    State S3: three 1s detected

## Slide 20: Example 1: Sequence Detector
Step 2: state assignment
  Two flip-flops
  Binary state coding
Step 3: Binary coded
state table
  Name flip-flops A and B
Step 4: Choose type of
flip-flops
  E.g., D flip-flop
  Characteristic equation: Q(t+1)=DQ

## Slide 21: Example 1: Sequence Detector
Step 6: derive flip-flop input equations and output equation
  Use state table

## Slide 22: Example 1: Sequence Detector
Step 6b: minimize equations

## Slide 23: Example 1: Sequence Detector

## Slide 24: Summary
Flip flops contain state information
State can be represented in several forms:
  State equations
  State table
  State diagram
Possible to convert between these forms
Circuits with states can take on a finite set of values
  Finite state machine
Two types of “machines”
  Mealy machine
  Moore machine