## Slide 1: Boolean Algebra Lecture 06 Book Chapter(s): 2
COE211-Digital Logic Design
Fall2020-الفصل الدراسي الأول 1442
جامعة طيبة فرع ينبع - كلية علوم وهندسة الحاسبات – شطر الطالبات
د. فاطمة الحربي

## Slide 2: Introduction
Boolean algebra forms the basis of logic circuit design.
Consider very simple but common example:
  if (A is true) and (B is false) then print “the solution is found”. In this case, two Boolean expressions (A is true) and (B is false) are related by a connective ‘and’. How do we define these? This and related things are discussed in this chapter.
In typical circuit design, there are many conditions to be taken care of:
  For example, when the ‘second counter’ = 60, the ‘minute counter’ is incremented and ‘second counter’ is made 0.
Thus it is quite important to understand Boolean algebra.
In subsequent chapters, we are going to further study how to minimize the circuit using laws of Boolean algebra  that is very interesting!

## Slide 3: Digital Circuits (1)
Digital circuit: can be represented by a black-box with inputs on one side, and outputs on the other:
The input/output signals are discrete/digital in nature, typically with two distinct voltages (a high voltage and a low voltage):
In contrast, analog circuits use continuous signals
Digital circuit
inputs
outputs
:
:
High
Low

## Slide 4: Digital Circuits (2)
Advantages of Digital Circuits over Analog Circuits:
  more reliable (simpler circuits, less noise-prone)
  specified accuracy (determinable)
  but slower response time (sampling rate)
Important advantages for two-valued Digital Circuit:
  Mathematical Model – Boolean Algebra
  Can help design, analyse, simplify Digital Circuits

## Slide 5: Boolean Algebra (1)
Boolean Algebra named after George Boole who used it to study human logical reasoning – calculus of proposition
Events : true or false
Connectives : a OR b; a AND b, NOT a
Example: Either “it has rained” OR “someone splashed water”, “must be tall” AND “good vision”.
What is an Algebra? (e.g. algebra of integers)
set of elements (e.g. 0,1,2,..)
set of operations (e.g. +, -, *,..)
postulates/axioms (e.g. 0+x=x,..)

## Slide 6: Boolean Algebra (2)
Later, Shannon introduced switching algebra (two-valued Boolean algebra) to represent bi-stable switching circuit

## Slide 7: Two-Valued Boolean Algebra
Set of Elements: {0,1}
Set of Operations: { ., + , ¬ }
Signals: High = 5V = 1; Low = 0V = 0
Sometimes denoted by ’, for example a’
x
y
x.y
x
y
x+y
x
x'

## Slide 8: Boolean Algebra Postulates (1)
A Boolean algebra consists of a set of elements B, with two binary operations {+} and {.} and a unary operation {'}, such that the following axioms hold:
  The set B contains at least two distinct elements x and y
  Closure: For every x, y in B,
    x + y is in B
    x . y is in B
  Commutative laws: For every x, y in B,
    x + y = y + x
    x . y = y . x

## Slide 9: Boolean Algebra Postulates (2)
Associative laws: For every x, y, z in B,
  (x + y) + z = x + (y + z) = x + y + z
  (x . y) . z = (x . y) . z = x . y . z
Identities (0 and 1):
  0 + x = x + 0 = x for every x in B
  1 . x = x . 1 = x for every x in B
Distributive laws: For every x, y, z in B,
  x . (y + z) = (x . y) + (x . z)
  x + (y . z) = (x + y) . (x + z)

## Slide 10: Boolean Algebra Postulates (3)
Complement: For every x in B, there exists an element x' in B such that:
  x + x' = 1
  x . x' = 0
The set B = {0, 1} and the logical operations OR, AND and NOT satisfy all the axioms of a Boolean algebra
A Boolean function maps some inputs over {0,1} into {0,1}
A Boolean expression is an algebraic statement containing Boolean variables and operators

## Slide 11: Precedence of Operators
To lessen the brackets used in writing boolean expressions, operator precedence can be used
Precedence (highest to lowest): ' . +
Examples:
a . b + c = (a . b) + c
b' + c = (b') + c
a + b' . c = a + ((b') . c)

## Slide 12: How to change the precedence?
Use brackets to overwrite precedence.
Examples:
a . (b + c)
(a + b)' . c

## Slide 13: Truth Table (1)
Provides a listing of every possible combination of inputs and its corresponding outputs.
Example (2 inputs, 2 outputs):

## Slide 14: Truth Table (1)
Example (3 inputs, 2 outputs):

## Slide 15: Proof using Truth Table
Can use truth table to prove by perfect induction
Prove that: x . (y + z) = (x . y) + (x . z)
Construct truth table for LHS & RHS of above equality:
Check that LHS = RHS:
Postulate is SATISFIED because output column 2 & 5 (for LHS & RHS expressions) are equal for all cases.

## Slide 16: Duality (1)
Duality Principle: every valid Boolean expression (equality) remains valid if the operators and identity elements are interchanged, as follows:
+  .
1  0
Example: Given the expression
a + (b.c) = (a+b).(a+c)
then its dual expression is
a . (b+c) = (a.b) + (a.c)

## Slide 17: Duality (2)
Duality gives free theorems – “two for the price of one” You prove one theorem and the other comes for free!
If (x+y+z)' = x'.y'.z' is valid, then its dual is also valid:
(x.y.z)' = x'+y’+z’
If x + 1 = 1 is valid, then its dual is also valid:
x . 0 = 0