## Slide 1: Karnaugh Maps Lecture 10
COE211-Digital Logic Design
Fall2020-الفصل الدراسي الأول 1442
جامعة طيبة فرع ينبع - كلية علوم وهندسة الحاسبات – شطر الطالبات
د. فاطمة الحربي

## Slide 2: Introduction
The Karnaugh map (k-map) is a systematic method to obtain simplified sum-of-products (SOPs) Boolean expressions
It is a special form of a truth table which enables easier pattern recognition
Objective: Fewest possible terms/literals
Diagrammatic technique based on a special form of Venn diagram
Advantage: Easy with visual aid
Disadvantage: Limited to 5 or 6 variables. However, it is usually good for designing circuits with up-to 4 variables

## Slide 3: Ven Diagrams (1)
Venn diagram to represent the space of minterms
Example of 2 variables (4 minterms):
ab'
a'b
a'b'
ab
a
b

## Slide 4: Venn Diagrams (2)
Each set of minterms represents a Boolean function
Examples:
  { ab, ab’ }  ab + ab' = a(b+b') = a
  { a'b, ab }  a'b + ab = (a'+a)b = b
  { ab }  ab
  { ab, ab', a'b }  ab + ab' + a'b = a + b
  { }  0
  { a'b',ab,ab',a'b }  1
ab'
a'b
a'b'
ab
a
b

## Slide 5: 2-Variable K-Maps (1)
Karnaugh-map (K-map) is an abstract form of Venn diagram, organised as a matrix of squares, where
  each square represents a minterm
  adjacent squares always differ by just one literal (so that the unifying theorem may apply: a + a' = 1)
For 2-variable case (e.g.: variables a,b), the map can be drawn in different forms as shown in the next slide 

## Slide 6: 2-Variable K-Maps (2)
Alternative layouts of a 2-variable (a, b) K-map:
a'b'
ab'
a'b
ab
b
a
m0
m2
m1
m3
b
a
OR
Alternative 2:
a'b'
a'b
ab'
ab
a
b
m0
m1
m2
m3
a
b
Alternative 1:
OR
ab
a'b
ab'
a'b'
b
a
m3
m1
m2
m0
b
a
OR
Alternative 3:
and others…

## Slide 7: 2-Variable K-Maps (3)
Equivalent labeling:
a
b
equivalent to:
a
b
0 1
0
1
b
a
equivalent to:
b
a
1 0
0
1

## Slide 8: 2-Variable K-Maps (4)
The K-map for a function is specified by putting:
  a ‘1’ in the square corresponding to a minterm
  a ‘0’ otherwise
For example: Carry and Sum of a half adder.
0
0
0
1
a
b
0
1
1
0
a
b
C = ab
S = ab' + a'b

## Slide 9: Example 1
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
OR Gate

## Slide 10: 3-Variable K-Maps (1)
There are 8 minterms for 3 variables (a, b, c). Therefore, there are 8 cells in a 3-variable K-map
ab'c'
ab'c
a
b
abc
abc'
a'b'c'
a'b'c
a'bc
a'bc'
0
1
00 01 11 10
c
a
bc
OR
m4
m5
a
b
m7
m6
m0
m1
m3
m2
0
1
00 01 11 10
c
a
bc
Note Gray code sequence
Above arrangement ensures that minterms of adjacent cells differ by only ONE literal. (Other arrangements which satisfy this criterion may also be used)

## Slide 11: 3-Variable K-Maps (2)
There is wrap-around in the K-map:
  a'b'c' (m0) is adjacent to a'bc' (m2)
  ab'c' (m4) is adjacent to abc' (m6)
m4
m5
m7
m6
m0
m1
m3
m2
0
1
00 01 11 10
a
bc
Each cell in a 3-variable K-map has 3 adjacent neighbours. In general, each cell in an n-variable K-map has n adjacent neighbours. For example, m0 has 3 adjacent neighbours: m1, m2 and m4.

## Slide 12: Example 2
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 | 0 | 1 | 1
1 | 1 | 1 | 1
A
0
1
BC
00 01 11 01

## Slide 13: 4-Variable K-Maps (1)
There are 16 cells in a 4-variable (w, x, y, z) K-map
m4
m5
w
y
m7
m6
m0
m1
m3
m2
00
01
11
10
00 01 11 10
z
wx
yz
m12
m13
m15
m14
m8
m9
m11
m10
x

## Slide 14: 4-Variable K-Maps (2)
There are 2 wrap-arounds:
  a horizontal wrap-around
  a vertical wrap-around
Every cell thus has 4 neighbours.
  For example, the cell corresponding to minterm m0 has neighbours m1, m2, m4 and m8.
m4
m5
w
y
m7
m6
m0
m1
m3
m2
z
wx
yz
m12
m13
m15
m14
m8
m9
m11
m10
x

## Slide 15: 5-Variable K-Maps (1)
Maps of more than 4 variables are more difficult to use because the geometry (hyper-cube configurations) for combining adjacent squares becomes more involved
For 5 variables, e.g. vwxyz, need 25 = 32 squares

## Slide 16: 5-Variable K-Maps (2)
Organised as two 4-variable K-maps:
m20
m21
w
y
m23
m22
m16
m17
m19
m18
00
01
11
10
00 01 11 10
z
wx
yz
m28
m29
m31
m30
m24
m25
m27
m26
x
m4
m5
w
y
m7
m6
m0
m1
m3
m2
00
01
11
10
00 01 11 10
z
wx
yz
m12
m13
m15
m14
m8
m9
m11
m10
x
v '
v
Corresponding squares of each map are adjacent.
Can visualise this as being one 4-variable map on TOP of the other 4-variable map.

## Slide 17: Larger K-Maps
6-variable K-map is pushing the limit of human “pattern-recognition” capability.
K-maps larger than 6 variables are practically unheard of!
Normally, a 6-variable K-map is organised as four 4-variable K-maps, which are mirrored along two axes.